## Slide 1: Minimap
RIT North Star + Lockheed Martin
Benjin Dubishar, Chris Carey, Josh Osgood, JP Mardelli
Prof. John Loser, Paul Mittan
3 December, 2013

## Slide 2: Product
what we’re making

## Slide 3: Context
large, indoor venues
  science, career fairs
  hundreds of presentations
teams of judges
difficult for judges to navigate

## Slide 4: Project Definition
“The goal of this project is to design and implement an electronic tracking system similar to a portable GPS that can be used inside a large room / building (i.e. gymnasium). The system should behave similar to a GPS, where an indicator for the location of the device will autonomously update its position as it is moving around a large room.”
- Project proposal

## Slide 5: Project Definition
“similar to a portable GPS” - why not GPS?
  consumer device accuracy
  buildings/indoors interference
  satellite acquisition time

## Slide 6: Project Definition
System to assist judges in navigating to their objectives
Tablet app, positioning system
  Position broadcasting, syncing
  High-fidelity, low-latency

## Slide 7: Scope
Within Scope
  Map creation tool
  Itinerary ingestion tool
  Tracking user position and displaying it on map
  Displaying all user positions on map
Outside scope
  Syncing itinerary checklists
  Storing user data about itinerary points (e.g. scores for projects)

## Slide 8: Requirements Elicitation
Sponsor interview
High-level architecture
Iterative UI mockups
List of questions/concerns

## Slide 9: Core Requirements
User position tracking, map display
Server for client communication and synchronization
Map creation/ingestion
Client position broadcast
Itinerary creation and display
Stable
Volatile

## Slide 10: Non-Functional Requirements
Accuracy
Latency
Cost
Usability
Open Source

## Slide 11: Architecture Design
Server coordinating data
Positioning refinement support
Multiple concurrent devices
Cartographer
Itinerary Creator

## Slide 12: Operational Design
Indoor Localization via triangulation or trilateration

## Slide 13: Trade Study

## Slide 14: Technology Selection - Trade Study
“The first goal of the student team would be to evaluate a minimum of three possible solutions to this problem, looking at past examples or other research and performing a Trade Study to determine the most appropriate approach given the constraints of this project (technical competence, cost and schedule).”
- Project proposal

## Slide 15: Trade Study
6 research papers reviewed
12 projects surveyed
16 page Trade Study document produced (2923 words)

## Slide 16: Terms to Know
Received Signal Strength Indication
  drop-off value measured in decibels
Time-of-Flight
  Time for a networking packet to travel between a server and client
Trilateration
  Location determination technique using distances from multiple points

## Slide 17
WiFi Signal Strength (RSSI)
WiFi Time-of-Flight (ToF)
Bluetooth Signal Strength (RSSI)
Ultrasonic Trilateration
Technology Selection - Trade Study
Notes: (Chris)

## Slide 18: Technology Selection - WiFi RSSI
Availability
Android compatibility
Poor accuracy
No iOS compatibility
Notes: (Chris)
Availability
  Low cost
Android Compatibility
  Supported by all Android devices/versions
Poor Accuracy
  Improved by fingerprinting
    Processing power
    Calibration
    Developer experience
Unavailable on iOS

## Slide 19: Technology Selection - WiFi ToF
Low computational complexity
Unachievable time precision required
Hardware configurability
Notes: (Chris)
Availability
  Low cost
Android Compatibility
  Supported by all Android devices/versions
Poor Accuracy
  Improved by fingerprinting
    Processing power
    Calibration
    Developer experience
Unavailable on iOS

## Slide 20: Technology Selection - Bluetooth
Low cost
Scalability
Accuracy
Cross-platform compatibility
Hardware requirements
Notes: (Chris)
Availability
  Low cost
Android Compatibility
  Supported by all Android devices/versions
Poor Accuracy
  Improved by fingerprinting
    Processing power
    Calibration
    Developer experience
Unavailable on iOS

## Slide 21: Technology Selection - Ultrasonic
Achievable precision
Cross-platform compatibility
Implementation complexity
High cost
Health concerns
Notes: (Chris)
Availability
  Low cost
Android Compatibility
  Supported by all Android devices/versions
Poor Accuracy
  Improved by fingerprinting
    Processing power
    Calibration
    Developer experience
Unavailable on iOS

## Slide 22
 | Accuracy | Cost | Difficulty | Overall
RSSI Trilateration | 1 | 9 | 8 | 5.1
ToF Trilateration | 4 | 8 | 2 | 4.8
Trilateration | 8 | 5 | 9 | 7.5
Trilateration | 10 | 1 | 2 | 5.7
Radio Field ID | Not viable – not on consumer devices |  |  | 
Near-Field Comm. | Not viable – max range 10cm |  |  | 
Technology Selection - Comparison
Notes: (Chris)

## Slide 23: Technology Choices - Platforms
Android 4.3
ASP.NET Web API

## Slide 24: Testing
Testing against ground truth
Accuracy thresholds
Calibration or adjustments
Tracking position in different environments (alone, crowded, obstacles)
= expected
= observed

## Slide 25: Risk Management - Technical Risks
No Platform Independent Solution Exists
Mitigation: Fallback to Android
Limited Android Experience
Mitigation: Allot time for self-learning
Incapable Hardware
Mitigation: Early implementation and testing

## Slide 26: Risk Management - Budget Risks
Limited Budget or Delay in Hardware Acquisition
Mitigation: Fallback on owned devices

## Slide 27: Risk Management - Schedule Risks
Scope Creep Mitigation: Assess priority and difficulty of all new requirements

## Slide 28: Process
how we’re making it

## Slide 29: Process - Development
Project Concerns
Adapt to changing requirements
  Capabilities of server
Mitigate risk
  Viability of trilateration technologies
  Hardware availability
Spiral Development
  Collection of Agile methodologies
  Address risk before each sprint
  Plan around risk and hardware availability
  Adapt to new requirements
  Internal task prioritization

## Slide 30: Scheduling
Client
Week 5-6: Android Skeleton Setup
Week 7-8: Wi-Fi Triangulation Exploration
Week 9-10: Other Technology Exploration
Week 11-12: UI Navigation
Week 13-14: Bluetooth RSSI/Distance Readings, Map with Beacons
End Goal (10): Technology Chosen
End Goal (15): Receive Map, Display Map, Location on Map
Control
Week 5-6: Choose Technology
Week 7-10: Focus on Client
Week 11-12: Ingest Map Configuration
Week 13-14: Collect Locations
End Goal: Deliver Map to Client

## Slide 31: Process - UI Design
Review Requirements
UI Wireframe Cycles
    Each member draws a wireframe individually
    Each member shares their wireframe with the group
    Repeat until convergence
Convert to high-fidelity mock-ups for sponsor review
Notes: (Chris)

## Slide 32: Process - UI Design Example
Round 1
Round 2
Notes: (Chris)

## Slide 33
Notes: (Chris)

## Slide 34
Notes: (Chris)

## Slide 35
Notes: (Chris)

## Slide 36: Metrics

## Slide 39: Implementation Status
UI scaffolding (double-drawer)
Bluetooth-reading prototypes
REST request from client app
Standalone server
  exposed through RESTful API

## Slide 40: Reflection
Efficient meetings and information transfer
UI design sessions
Straightforward architecture
Learn from past attempts
Brand new technology
Android development ramp-up
Unstable Android emulators

## Slide 41: Future <Josh?>

## Slide 42: Minimap
Benjin Dubishar
Chris Carey
Josh Osgood
JP Mardelli