## Slide 1: Research Review
Team North Star + Lockheed Martin

## Slide 2: Terms to Know
WiFi/802.11
  Wireless communication specification for operation in the 2.4, 3.6, 5, and 60 GHz frequency bands.
Bluetooth
  Short-distance wireless communication specification for operation between 2400-2480 MHz.
RSSI
  Received Signal Strength Indication

## Slide 3: Terms to Know (Continued)
Trilateration
  Using geometry to determine the position of a point in relation to three or more known anchor points.
Fingerprinting
  Comparing measurements against a calibrated map which matches them to an approximate position.
Time of Flight
  The time it takes for a data packet to travel from a sending device to a receiving device.

## Slide 4: Potential Solutions Surveyed
WiFi RSSI
WiFi Time-of-Flight
Bluetooth RSSI
Ultrasonic Trilateration
Near-Field Communication Array
Radio Frequency ID Array
All WiFi and Bluetooth techniques involve trilateration and can be refined by fingerprinting

## Slide 5: WiFi RSSI - Overview
Distributed WiFi Access Points
  Device collects SSID and RSSI
  Calculates distance using RSSI
    Non-linear correlation
    Easily affected by environmental factors
  Calculates position using trilateration
Enhanced by Fingerprinting

## Slide 6: WiFi RSSI - Past Attempts
System | Best Accuracy | Mobile Capable
Skyhook (Wi-Fi) | 10 m | Yes
Navizon (Wi-Fi) | 20 m | Yes
Gaussian Processes for Signal Strength-Based Location Estimation (Ferris, 2006) | 2 m | Yes
Ekahau | 1 m | No

## Slide 7: WiFi RSSI - Advantages
Android Compatibility
  Supported by all Android devices/versions
Availability
  Competitive market
  Low cost

## Slide 8: WiFi RSSI - Disadvantages
Poor Accuracy
  Improved by fingerprinting
    Processing power
    Calibration
    Developer experience
Unavailable on iOS
  Not exposed in SDK

## Slide 9: WiFi Time of Flight - Overview
Distributed WiFi Access Points
  Server sends timestamped packet to device
  Device calculates packet travel time
    Correlates linearly to distance
  Calculates position using trilateration
Enhanced by Fingerprinting

## Slide 10: WiFi Time of Flight - Past Attempts
System | Best Accuracy | Smartphone Capable
Goodtry | 4 m | No
Multipath Mitigation for Indoor Localization Based on IEEE 802.11 Time-of-Flight Measurements | 0.7* m | No

## Slide 11: WiFi Time of Flight - Advantages
Low Complexity
  Simple computation
    Time of Flight x Speed of Light
  More complex with fingerprinting

## Slide 12: WiFi Time of Flight - Disadvantages
Synchronization
  Short distance between device and access point
  Requires unachievable precision
Specialized hardware or inefficient algorithm

## Slide 13: Bluetooth RSSI - Overview
Distributed Bluetooth Beacons
  Device collects SSID and RSSI
  Calculates distance using RSSI
  Calculates position using trilateration
Enhanced by Fingerprinting

## Slide 14: Bluetooth RSSI - Past Attempts
System | Best Accuracy | Smartphone Capable
Bluetooth Direction of Arrival | 72 cm | No
Nokia High Accuracy Indoor Positioning System | 20 cm | Not yet
A Comprehensive Study of Bluetooth Fingerprinting-Based Algorithms for Localization (Zhang et. al., 2013) | < 1 m | No

## Slide 15: Bluetooth RSSI - Advantages
Availability
  Low cost per beacon
Scalable
Accuracy
  Not dependent on fingerprinting
Cross-Platform Compatibility

## Slide 16: Bluetooth RSSI - Disadvantages
Compatibility
  Bluetooth 4.0 Low Energy not supported by older devices
Cost
  Newer devices
  Multiple beacons

## Slide 17: Ultrasonic Trilateration - Overview
Distributed Ultrasonic Emitters
  Device detects ultrasonic chirps
    Two techniques:
      Calculates chirp travel time, identifying via pattern
      Calculates amplitude, different anchor points have different frequencies
    Correlates linearly to distance
  Calculates position using trilateration

## Slide 18: Ultrasonic Trilateration - Past Attempts
System | Best Accuracy | Smartphone Capable
The Bat | 3 cm | No
The Cricket | 3 cm | No
Lok8 (Filonenko, et. al. 2012) | < 1 m | Yes

## Slide 19: Ultrasonic Trilateration - Advantages
Achievable Synchronization
  Based on sound waves
  Requires less precision due to slower speed of propagation
Cross-Platform Compatibility

## Slide 20: Ultrasonic Trilateration - Disadvantages
Complex Implementation
  Potentially difficult synchronization
  Custom method of identifying emitters ultrasonically
  Specialized hardware or constant Fourier math (computationally expensive; battery life implications)
  Additional software for controlling sound emitters
Cost
Health Concerns

## Slide 21: Near-Field Communication Array
Impractical
  Extremely short range - 2 cm

## Slide 22: Radio Frequency ID Array
Impractical
  Not supported by mobile devices
  Short range
  Expensive

## Slide 23: Comparison
System | Optimal Accuracy Rating | Hardware Cost | Ease of Implementation | Overall Score
Wi-Fi RSSI Trilateration | 1 | 9 | 8 | 5.1
Wi-Fi RSSI Fingerprinting | 3 | 9 | 5 | 5.5
802.11 ToF Trilateration | 4 | 8 | 2 | 4.8
802.11 ToF Fingerprinting | 5 | 8 | 1 | 5.1
Bluetooth 4.0 Connectivity | 9 | 1 | 10 | 7.3
Bluetooth 4.0 Trilateration | 8 | 5 | 9 | 7.5
Bluetooth 4.0 Fingerprinting | 8 | 5 | 5 | 6.5
Ultrasonic Trilateration | 10 | 1 | 2 | 5.7

## Slide 24: Recommendation: Bluetooth
Accuracy
  More consistent readings
Scalability
  Simply add more beacons
Cross-Platform Compatibility
Competitive Cost
Straightforward Implementation
Newer Technology

## Slide 25: Bluetooth Beacon Layout
N
~ 1.8 N

## Slide 26: Bluetooth Beacons
Name | Maximum Range | Unit Price | Website
Stick-’n’-Find | 30 m | $20 ($390 for 20) | https://sticknfind.com
Estimote | 50 m | $33 ($99 for 3) | http://estimote.com
Tod | 100 m | $38 ($380 for 10) | http://todhq.com
Roximity | ? | $10 / month (or inquiry) | http://buyibeacons.com/
Adomaly | ? | By inquiry | https://adomaly.com/
Accuracy is inversely proportional to maximum range

## Slide 27: Estimated Costs
Stick-’n’-Find
  4 beacons = $90, minimum for development + testing
  ⌈9⌉ beacons = $200, minimum (estimated) for covering RIT’s Gordon Field House floor; more beacons = more accurate
Nexus 7
  At least 2 @ $230 each for testing
  Requires newest model for Bluetooth Low Energy compatibility

## Slide 28: Questions